## Slide 1: High Performance Message Passing Infiniband Communication Devices for Java HPC
Authors:
  Omar Khan
  Mohsan Jameel
  Aamir Shafi
School of Electrical Engineering and Computer Science (SEECS)
National University of Sciences and Technology, (NUST) Pakistan

## Slide 2: Agenda
Introduction to MPJ Express:
  MPJ Express
  Java HPC
  MPJ Express Configurations
  MPJ Express Architecture
  Contributions of this Paper
InfiniBand Device
Performance Evaluation
Summary

## Slide 3: Introduction to MPJ Express
MPJ Express is an MPI-like library that supports execution of parallel Java applications:
  http://mpjexpress.org
    The Java Grande Forum—formed in late 90s—came up with an API called mpiJava 1.2
      MPJ Express implements this API
Motivation for a new Java messaging system:
  Maintain compatibility with Java threads by providing thread-safety
  Handle contradicting issues of high-performance and portability
  Requires no change to the native standard JVM
Notes: MPJ Express is thread safe Message Passing System in Java. It is based on MPI Like standard mpiJava 1.2.
MPJ Express provides two modes of message passing. One is multicore modes. This mode developed for Shared memory and multicore processors. It is build on Java threads and these threads acts as MPJ Express processes and communicate through high speed shared memory communication mechanism.
Second mode is known as cluster mode. In this mode is based on Distributed Memory parallelism. All parallel processes are distributed and communication is done by message passing over the network.
This mode provides two network devices. One is niodev that is built on Java New IO technology and it work on TCP/IP.
Second device is mxdev that is built for high speed Myrinet interconnect.

## Slide 4: Why Java
Portability
A popular language in colleges and software industry:
  Large pool of software developers
  A useful educational tool
Higher programming abstractions including OO features
Improved compile and runtime checking of the code
Automatic garbage collection
Support for multithreading
Rich collection of support libraries
Hadoop: A successful Java based distributed computing platform.

## Slide 5: Communication Devices in MPJ Express
MPJ Express Modes
Multicore mode
Java NIO
Myrinet Express
Native MPI library
Java Threads
Cluster mode
InfiniBand
Multicore mode
Cluster mode

## Slide 6: InfiniBand Support in Java
No direct support in Java to fully exploit InfiniBand.
Currently relies on TCP/IP emulation for communication over IB network
For Giga-bit Ethernet, bandwidth and latency performance of Java nearly the same as that of C .
  Java Runtime and Java TCP/IP stacks are well optimized
  Comparable with C/C++ in network Intensive I/O
For InfiniBand, the TCP/IP emulation layers show poor performance.
SDP and IPoIB are example of ULP’s (Upper Layer Protocols)
 | IB Verbs | SDP | IPoIB
API | Low level | Socket (TCP only) | Socket
Latency | Lowest | Lower | Low
Bandwidth | Highest | High | Medium
CPU utilization | Lowest | High | highest
Kernel bypass |  |  | 
ULP overhead | Light | Medium | High
Memory registration | Explicitly by application/ middleware | Heuristics by SDP | None
Application adaptation | Porting/development required | Supports unmodified application | 

## Slide 7: Other MPI Libraries for Java
FastMPJ is a proprietary implementation of mpiJava 1.2 API with following communication devices:
  Ethernet
  SMP
  Myrinet
  InfiniBand
Open MPI has introduced Java Bindings using JNI
  Uses Open MPI as native MPI library

## Slide 8: Contributions of this Paper
MPJ Express layered Architecture
Ibdev bypass the TCP/IP emulation laryer by directly interfacing with IB Verbs API through Java Native Interface
  Offload communication to the InfiniBand Hardware
  Avoids extra overhead introduced by TCP/IP emulation incurred by ULPs

## Slide 9: Agenda
Introduction to MPJ Express
InfiniBand Device:
  Design
  Functionality
  Point-to-Point Communication
Performance Evaluation
Summary

## Slide 10: ibdev – InfiniBand Device for MPJ Express
InfiniBand device in xdev layer
Java Native Interface (JNI) wrapper to access low level native code
Each method of ibdev delegates on a native function
xdev layer
ibdev
JNI
IBV C Library
libibverbs + librdmacm
InfiniBand Hardware
Java
C

## Slide 11: ibdev – Native C library
Built on top of Verbs API
Implements a set of low-level communication primitives, which are in turn used by the higher layers
Connected Transport Service
  Reliability
  Delivery order
  Data loss detection
  Error detection
xdev layer
ibdev
JNI
IBV C Library
libibverbs + librdmacm
InfiniBand Hardware
Java
C

## Slide 12: ibdev - Native C library - Initialization
Connection manager is used to setup connection between all processes.
Set of Queue Pair QP (Send and Recv Queues) and a Completion Queue CP are created for evey connection at each process.
Example of three processes initialization
P0
P1
P2
InfiniBand Device
CQ
QP
Send
Recv
InfiniBand Device
CQ
QP
Send
Recv
InfiniBand Device
CQ
QP
Send
Recv
Connection Request
Connection Request
Connection Request
Accept Connection
Accept Connection
Accept Connection
Device Initialized
InfiniBand Device
CQ
QP
Send
Recv
InfiniBand Device
CQ
QP
Send
Recv
InfiniBand Device
CQ
QP
Send
Recv

## Slide 13: Point to Point Communication
InfiniBand Device
CQ
QP
Send
Recv
Memory Segment
Memory Segment
Memory registered for CM
Processor
Registered Send Buffer
InfiniBand Device
CQ
QP
Send
Recv
Memory Segment
Memory Segment
Memory registered for CM
Registered Receive Buffer
Processor
Registers send buffer
Sends MSG_MR CM to receiver
  Tag, context, buffer length
Gets control message from sender
Registers memory buffers
Sends MSG_RDY CM containing memory keys to sender
Gets remote keys of the receive buffer in control message
RDMA write to remote memory
Sender
Receiver
Communication Completed

## Slide 14: Communication Protocols
Registration of buffer prior to communication
  Involves OS and NIC
  Expensive operation
Eager protocol
  Small messages < 128K
  Avoid buffer registration
  Pool of pre-registered buffers
Rendezvous protocol
  Large messages > 128K
  Buffer pinned on the fly
  Unregistered after use
  Remote keys exchanged via control messages

## Slide 15: Agenda
Introduction to MPJ Express:
InfiniBand Device
Performance Evaluation:
  Point-to-Point Communication
  Java NAS Parallel Benchmarks
Conclusion and Future Work

## Slide 16: Point-to-Point Latency
Latency in µsec
Chart: Message Size in Bytes
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K
MPJ Express - ibdev (Buffering) | 34 | 28 | 27 | 27 | 27 | 27 | 27 | 27 | 27 | 27 | 28 | 30
MPJ Express - ibdev (w/o Buffering) | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 12
MPJ Express - IPoIB | 89 | 42 | 87 | 88 | 71 | 86 | 36 | 71 | 67 | 109 | 52 | 31
OpenMPI | 2.29 | 2.29 | 2.3 | 2.35 | 2.36 | 2.42 | 2.7 | 4.26 | 4.63 | 27 | 5.72 | 7.32
MPJ Express - SDP | 338 | 324 | 327 | 329 | 330 | 331 | 334 | 334 | 335 | 334 | 336 | 347

## Slide 17: Point-to-Point Bandwidth
Chart: Message size in Bytes
| 2K | 4K | 8K | 16K | 32K | 64K | 128K | 256K | 512K | 1M | 2M | 4M | 8M | 16M
OpenMPI | 2.3992 | 3.9237 | 5.9333 | 9.2065 | 12.9879 | 16.0159 | 19.5059 | 20.0132 | 23.6197 | 24.0003 | 24.0003 | 25.5997 | 25.6002 | 23.996
MPJ Express - ibdev (Buffering) | 0.52083 | 1.0081 | 1.7361 | 2.7778 | 3.9683 | 5.2083 | 10.5263 | 12.7389 | 14.5985 | 15.5945 | 16.0966 | 14.9883 | 13.7812 | 14.0182
MPJ Express - IPoIB | 1.0081 | 0.37425 | 0.3125 | 0.50302 | 0.49116 | 1.1682 | 0.57356 | 0.78201 | 0.92593 | 0.75568 | 0.82897 | 0.82038 | 0.80277 | 0.84837
MPJ Express - ibdev (w/o Buffering) | 1.3021 | 2.4038 | 4.1667 | 6.25 | 8.6207 | 10.4167 | 14.0845 | 18.018 | 21.164 | 22.8571 | 23.9163 | 23.8273 | 22.6629 | 23.9163
MPJ Express - SDP | 0.090058 | 0.17756 | 0.33784 | 0.65274 | 1.1442 | 4.5455 | 2.0921 | 2.4331 | 6.1824 | 7.1975 | 7.4194 | 6.4406 | 6.2754 | 6.4856

## Slide 18: Java NAS Parallel Benchmark
Chart: MOPS
| 1 | 2 | 4 | 8 | 16 | 32 | 64
MPJ Express - ibdev | 1140 | 2024 | 3274 | 5006 | 9543 | 12781
MPJ Express - SDP | 500 | 1037 | 1724 | 2874 | 4206 | 7243 | 10343
MPJ Express - IPoIB | 345 | 589 | 1432 | 1905 | 2817 | 3936 | 3821
Chart: MOPS
| 1 | 2 | 4 | 8 | 16 | 32 | 64
MPJ Express - ibdev | 1005 | 1643 | 2433 | 3566 | 7589 | 15511 | 21431
MPJ Express - IPoIB | 700 | 1333 | 1900 | 3000 | 4201 | 6034 | 7513
MPJ Express - SDP | 900 | 1443 | 2133 | 3366 | 5839 | 11511 | 15431
Chart: MOPS
| 1 | 2 | 4 | 8 | 16 | 32 | 64
MPJ Express - ibdev | 112 | 135 | 198 | 255 | 412 | 677 | 851
MPJ Express - IPoIB | 79 | 94 | 131 | 170 | 224 | 285 | 40
MPJ Express - SDP | 102 | 126 | 168 | 225 | 361 | 573 | 701
CG Kernel (Class C)
FT Kernel (Class C)
IS Kernel (Class C)

## Slide 19: Agenda
Introduction to MPJ Express:
InfiniBand Device
Performance Evaluation
Summary

## Slide 20: Summary
Java message passing libraries should focus on low level communication devices for high speed interconnects.
Transparently provides MPJ Express with efficient performance on InfiniBand.
High performance because relies on native verbs to take advantage of RDMA support.

## Slide 21: Questions? http://mpjexpress.org